## Slide 1: SMART WATER SUPPLY MANAGEMENT
Presented By:
Sujata Gupta (21250)
Patil Sarvjit Ajit (20862)
Kirteyman Singh Rajput (21760)
Project: Design for Analog Electronics and Industrial Instrumentation

## Slide 2: Problem Statement
To automate the current water supply on rooftop tank in DESE
Sources of Supply
  Borewell
  IISc main water resource
Current Management
  Manual ON/OFF management

## Slide 3: Current Scenario
Submersible
P1
P2
T1
T2
DESE
From IISc main water resource
P: Pump
T: Tank

## Slide 4: Proposed Solution
Submersible
P1
P2
T1
T2
DESE
C
From IISc main water resource
P: Pump
T: Tank
C: Controller

## Slide 5: Components at Stages
T1,T2: Level Sensors, nRF24L01
P1,P2: nRF24L01, Pump Controller
C: nRF24L01, Display Message
Same nRF will be shared by T2 and P2

## Slide 6: nRF24L01
SPI Communication
Frequency Range: 2.4 GHz ISM band
Communication distance: 100 m
Operating Voltage: 1.9 - 3.6V
Rate: up to 2 Mbps
Current : 12 mA during transmission mode
  Less than a single LED (30 mA)
Specially designed for ultra low power applications
Image Courtesy: Google

## Slide 7: nRF24L01
Can use 125 different channels
Each channel has up to 6 addresses i.e. can use 6 other devices simultaneously
PRX: Primary Receiver
PTX: Primary Transmitter
The multi-receiver capacity of nRF24L01 is having up to 6 channels (pipes) of radio communication
  Receiving or read mode simultaneously
Each PTX node links to one of these pipes to use both in transmitting and receiving
Image Courtesy: Google

## Slide 8: Block Diagram of PCB
Microcontroller
AMS1117
Relay
nRF24L01
Power Supply
3.3 Volts
5 Volts
5 Volts
Water Pump
Water Level Sensor

## Slide 9
Thank You