## Slide 1: E3-258 Design for IoT Intrusion Detection System
Kirteyman Rajput
Sarvjit Ajit Patil

## Slide 2: Challenges:
Capturing signals with multiple sensors.
Size, cost and power requirements.
Choosing the right sensors.
Scope:
To detect intrusion in specific area.
Alert the concerned person.

## Slide 3: Applications:
Home Security
Intruder alert in exhibitions, jewellery shops, industries.
Perimetral Security.

## Slide 4: System Design

## Slide 5: Choosing the Sensor:
We want to detect vibrations and pressure sensitivity
Even smallest amplitude signal – high sensitivity and resolution.
In any environment e.g. sun, dark, fog, dust, temperature
With minimum power consumption.
With small form factor.

## Slide 6: Pressure-Sensitive Conductive Sheet( Velostat ):
Dimensions: 11" x 11" (280mm x 280mm)
4 mil / 0.1mm thick
Weight: 18.66g
Temperature Limits : -45°C to 65°C (-50°F to 150°F)
Volume Resistivity : <500 ohm-cm
Surface Resistivity : < 31,000 ohms/sq.cm
Why?
More area coverage with more matrix connections.
Doesn’t break on applying pressure (flexible).
High sensitivity.

## Slide 7
Interfacing Velostat sheet
Challenges:
Taking connections to interface with microcontroller.
Choosing resistor R.

## Slide 8
Implementation Plan

## Slide 9
Matrix Multiplexing allows coverage of more area with less GPIOs.
Write HIGH to each column and read each row at a time.
- Same as keypad matrix

## Slide 10
Fig. Seat cover fabric with copper tapes sticked.

## Slide 11
Engineering and Software Layout

## Slide 12: Interfacing Velostat:
Choosing R:
… nRF52840 datasheet
… ESP32 datasheet
Fig. Adding connections to velostat.
Fig. Interfacing velostat to microcontroller.

## Slide 13
Selected
Still,
Reading analog values with appropriate threshold.

## Slide 14: Detecting Human Steps
while (1) :
  Read nodes sequentially;
  Check whether a node has crossed threshold?
  If yes :
  check its nearby nodes (only above and below will work in this case)
      If any of these crossed threshold :
      human step is detected
  else :
  nop
Adjusted node positions such that two of them will give sufficiently high signal.

## Slide 15
Algorithm:
ESP32_Modem -> ON
Send init message
ESP32_Modem -> OFF
while (1) :
read all nodes
check with the auth_key
if true:
Authentication successful
ESP32_Modem -> ON
send a message to the user via Telegram
ESP32_Modem -> OFF
else:
Authentication failed
ESP32_Modem -> ON
send a message to the user via Telegram
ESP32_Modem -> OFF

## Slide 16
  Read nodes sequentially;
    Check whether a step is detected?
    If yes :
    ESP32_Modem -> ON
    send a message to the user via Telegram
    ESP32_Modem -> OFF
    else :
    nop

## Slide 17
Current Consumption
IDLE(Blank code dumped in ESP32):
WiFi and BLE ON:
Current Consumption
WiFi ON (While sending Message):
WiFi OFF:
Low Power Mode

## Slide 19
User Authentication

## Slide 20: Hardware
  ESP32
  -Computes steps and Communicates with smartphone.
  TP4056
  -Battery charging module.

## Slide 21: Software
Arduino IDE
To program ESP32.
  Library
WiFi
WiFiClientSecure
UniversalTelegramBot

## Slide 22
Demo Plan

## Slide 24
Thank You